## Slide 1: Tutorial 6
Implement and functionally simulate Full Adder circuit in Quartus tool using schematic and structural VHDL coding.

## Slide 2: FA using Structural VHDL
HA2
S
Cout
HA1
A
B
Full_adder
A
B
Cin
S
Cout
Cin
OR1
HA
X
Y
Sum
Carry
X
Y
Sum
Carry
X
Y
Sum
Carry
OR_gate
P
Q
Z
P
Q
Z

## Slide 3: VHDL Dataflow Model of Half Adder
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity HA is
Port ( X : in STD_LOGIC;
Y : in STD_LOGIC;
Sum : out STD_LOGIC;
Carry : out STD_LOGIC);
end HA ;
architecture dataflow of HA is
begin
Sum <= X XOR Y;
Carry <= (X AND Y) ;
end dataflow;
HA
X
Y
Sum
Carry

## Slide 4: VHDL Dataflow Model of OR gate
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity OR_gate is
Port ( P : in STD_LOGIC;
Q : in STD_LOGIC;
Z : out STD_LOGIC);
end OR_gate ;
architecture dataflow of OR_gate is
begin
Z <= P OR Q;
end dataflow;
OR_gate
P
Q
Z

## Slide 5
HA2
S
Cout
HA1
A
B
Cin
OR1
X
Y
Sum
Carry
X
Y
Sum
Carry
P
Q
Z
S1
S2
S3
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity Full_adder is
Port ( A : in STD_LOGIC;
B : in STD_LOGIC;
Cin : in STD_LOGIC;
S : out STD_LOGIC ;
Cout : out STD_LOGIC);
end Full_adder ;
architecture Structural of Full_adder is
component HA is
Port ( X : in STD_LOGIC;
Y : in STD_LOGIC;
Sum : out STD_LOGIC;
Carry : out STD_LOGIC);
end component;
component OR_gate is
Port ( P : in STD_LOGIC;
Q: in STD_LOGIC;
Z: out STD_LOGIC);
end component;
signal S1,S2,S3: STD_LOGIC;
begin
HA1: HA port map( A, B, S1, S2);
HA2: HA port map( S1, Cin, S, S3);
OR1: OR_gate port map( S3, S2, Cout);
end Structural ;