## Slide 1: Tutorial-2
VHDL Intro
Part-2

## Slide 2
“00”
01
10
11
architecture dataflow of mux_4to1N is
begin
process (A,B,C,D,S0,S1) is
begin
Z <=((NOT S0) AND (NOT S1) AND A) OR ((NOT S0) AND S1 AND B) OR (S0 AND (NOT S1) AND C) OR ( S0 AND S1 AND D);
end process;
end dataflow;

## Slide 3: VHDL Structural Model
Specifies what blocks (or components) are used and how they are interconnected.
It is a hierarchical design modelling in which one can define components of units that are used over and over again. This can significantly reduce the complexity of larger design.
VHDL provides a formal way to do this by
Declare a list of components being used
Declare signals which define the netlist (a netlist is a description of the connectivity of an electronic circuit) of interconnected components
Label multiple instances of the declared components so that each instance is uniquely defined.

## Slide 4: Architecture Template(Structural)
architecture architecture_name of NAME_OF_ENTITY is
-- Declarations
-- components declarations
-- signal declarations
begin
-- Statements
-- components instantiation and connections
:
end architecture_name;

## Slide 5: Component Declaration
component component_name is
port (port_signal_names: mode type;
port_signal_names: mode type;
:
port_signal_names: mode type);
end component component_name;

## Slide 6: Component Instantiation and Interconnection
Syntax is as follows:
Label: component _name Port map (signal1, signal2,…, signaln);
Signal positions must be in the same order as the declared component ports.
This method of port signals association is called positional association.

## Slide 7: Example: 4-bit adder
FA1
FA2
FA3
FA4
A(0)
B(0)
A(1)
A(2)
A(3)
B(1)
B(2)
B(3)
C0
C4
S(0)
S(1)
S(2)
S(3)
A
B
S
A
B
S
A
B
S
A
B
S
Cin
Cout
Cin
Cout
Cin
Cout
Cin
Cout
A=(0010)
B=(0001)
Sum=0011, carry=_

## Slide 8: VHDL Structural Model of 4-bit Adder
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity Ripple_Adder is
Port ( A : in STD_LOGIC_VECTOR (3 downto 0);
B : in STD_LOGIC_VECTOR (3 downto 0);
C0 : in STD_LOGIC;
S : out STD_LOGIC_VECTOR (3 downto 0);
C4 : out STD_LOGIC);
end Ripple_Adder;
architecture Structural of Ripple_Adder is
component full_adder is
Port ( A : in STD_LOGIC;
B : in STD_LOGIC;
Cin : in STD_LOGIC;
S : out STD_LOGIC;
Cout : out STD_LOGIC);
end component;
signal C1,C2,C3: STD_LOGIC;
begin
FA1: full_adder port map( A(0), B(0), C0, S(0), C1);
FA2: full_adder port map( A(1), B(1), C1, S(1), C2);
FA3: full_adder port map( A(2), B(2), C2, S(2), C3);
FA4: full_adder port map( A(3), B(3), C3, S(3), C4);
end Structural ;
FA1
FA2
FA3
FA4
A(0)
B(0)
A(1)
A(2)
A(3)
B(1)
B(2)
B(3)
C0
C4
S(0)
S(1)
S(2)
S(3)
A
B
S
A
B
S
A
B
S
A
B
S
Cin
Cout
Cin
Cout
Cin
Cout
Cin
Cout
C1
C2
C3

## Slide 9: VHDL Dataflow Model of Full Adder
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity full_adder is
Port ( A : in STD_LOGIC;
B : in STD_LOGIC;
Cin : in STD_LOGIC;
S : out STD_LOGIC;
Cout : out STD_LOGIC);
end full_adder;
architecture dataflow of full_adder is
begin
S <= A XOR B XOR Cin ;
Cout <= (A AND B) OR (Cin AND A) OR (Cin AND B) ;
end dataflow;
Full_adder
A
B
Cin
S
Cout

## Slide 10: FA using Structural VHDL
Full_adder
A
B
Cin
S
Cout

## Slide 11: FA using Structural VHDL
HA2
S
Cout
HA1
A
B
Full_adder
A
B
Cin
S
Cout
Cin
OR1

## Slide 12: FA using Structural VHDL
HA2
S
Cout
HA1
A
B
Full_adder
A
B
Cin
S
Cout
Cin
OR1
HA
X
Y
Sum
Carry
X
Y
Sum
Carry
X
Y
Sum
Carry
OR_gate
P
Q
Z
P
Q
Z

## Slide 13: VHDL Dataflow Model of Half Adder
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity HA is
Port ( X : in STD_LOGIC;
Y : in STD_LOGIC;
Sum : out STD_LOGIC;
Carry : out STD_LOGIC);
end HA ;
architecture dataflow of HA is
begin
Sum <= X XOR Y;
Carry <= (X AND Y) ;
end dataflow;
HA
X
Y
Sum
Carry

## Slide 14: VHDL Dataflow Model of OR gate
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity OR_gate is
Port ( P : in STD_LOGIC;
Q : in STD_LOGIC;
Z : out STD_LOGIC);
end OR_gate ;
architecture dataflow of OR_gate is
begin
Z <= P OR Q;
end dataflow;
OR_gate
P
Q
Z

## Slide 15
HA2
S
Cout
HA1
A
B
Cin
OR1
X
Y
Sum
Carry
X
Y
Sum
Carry
P
Q
Z
S1
S2
S3
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity Full_adder is
Port ( A : in STD_LOGIC;
B : in STD_LOGIC;
Cin : in STD_LOGIC;
S : out STD_LOGIC ;
Cout : out STD_LOGIC);
end Full_adder ;
architecture Structural of Full_adder is
component HA is
Port ( X : in STD_LOGIC;
Y : in STD_LOGIC;
Sum : out STD_LOGIC;
Carry : out STD_LOGIC);
end component;
component OR_gate is
Port ( P : in STD_LOGIC;
Q: in STD_LOGIC;
Z: out STD_LOGIC);
end component;
signal S1,S2,S3: STD_LOGIC;
begin
HA1: HA port map( A, B, S1, S2);
HA2: HA port map( S1, Cin, S, S3);
OR1: OR_gate port map( S3, S2, Cout);
end Structural ;